## Slide 1: Part II: Downlink Interference Analysis in Heterogeneous Cellular Networks using Stochastic Geometry
Yuan Liang

## Slide 2: Introduction
The traditional homogeneous network expansion technique, such as cell splitting, is inept at handling the growth in wireless communication since the deployment of macro base station (MBS) necessitates a huge capital expenditure (CAPEX). Under such circumstance, industries start to resort to other solutions, and the concept of small cells is proposed.
The term ``small cell'' refers to the low-power and low-cost radio access points operating in both licensed and unlicensed spectra, including femtocells, picocells, microcells and metrocells.

## Slide 3: Introduction
In order to accommodate more users using limited wireless spectrum resources, universal frequency reuse is often employed in heterogeneous networks. That is, the available spectrum will be aggressively reused by all of the network tiers.
Conventionally, the distribution of base stations (BSs) in homogeneous networks is assumed to follow a hexagonal grid model. However, such assumption in heterogeneous networks is not suitable because (i) the interference analysis may require massive Monte Carlo simulation which is intractable and (ii) due to the variation in demand among areas, the distribution of BSs in heterogeneous networks will have random patterns. Thus, new models for heterogeneous cellular networks are needed.

## Slide 4: Introduction
Recently, a new modeling approach basing on stochastic geometry is adopted in heterogeneous networks which can lead to tractable analytical results while keeping the randomness of network geometry. Stochastic geometry is a very powerful mathematical and statistical tool for the modeling, analysis and design of wireless networks with random topologies and has been applied in ad hoc networks for several decades

## Slide 5: Preliminaries
Consider a Euclidean space. A spatial Point Process (PP) is a random, finite or countably-infinite collection of points in the space.
A Poisson Point Process (PPP) is a PP where the numbers of points of any disjoint subsets are independent Poisson random variables.
Important properties:
Superposition and thinning
Palm theory
Stationaries

## Slide 6: Related Works
In , the authors compared the performance of a PPP and a square grid model to the performance of an actual deployed cellular network and showed that PPP can provide a lower bound on the coverage probability and the mean transmission rate obtained by measurements. Such comparison revealed the accuracy of PPP model and shed lights on the modeling and analysis of cellular wireless networks using stochastic geometry.
The conclusions of are: (a) the PPP model provides a relatively tight bound for the performance of actual network (b) simple expressions of coverage probability and mean transmission rate can be derived by using PPP model (c) when the noise is negligible in transmission, the SINR statistics are independent of the intensity of BSs.

## Slide 7: A Toy Example
Consider a two-tier cellular network consisting of macro tier (tier 1) and femto tier (tier 2). The distribution of MBSs and FAPs are independent homogeneous PPPs. Universal frequency reuse and F-ALOHA are employed, i.e., for each available frequency band or channel, each MBS and FAP will randomly access it with certain probabilities.

## Slide 8: A Toy Example
Coverage probability: A arbitrary user will be served by BS/AP of tier i at distance r with probability:

## Slide 9: A Toy Example
The signal-to-interference ratio (SIR) can be expressed by (suppose a user of tier 1 at distance r from the MBS)
The complementary cumulative distribution function (CCDF) of SIR conditioned on r is

## Slide 10: A Toy Example
The CCDF of SIR of an arbitrary user is
The spatial average of channel capacity is

## Slide 11: Numerical Results
Outage probability for different SIR threshold
Spatial average of channel capacity